The plots in PNG provide the quick-look display of the Level-1 ROCSAT-IPEI data for the day of interest (e.g., 01090 for 31 March 2001). Level-1 data are 1-sec averaged total ion density, ion temperature, relative ion composition in percent, and ion velocity in the magnetic field aligned local coordinate system (V||, and V⊥M as well as V⊥Z).

The velocity is in unit of m/s. V|| is the velocity component parallel to B.

V⊥M is one of the two components perpendicular to B and in the magnetic meridian plane. Positive V⊥M points upward/northward.  While V⊥Z is the perpendicular velocity component in the geomagnetic zonal direction.  Positive V⊥Z points eastward.

Local time variations of the 1-sec averaged IPEI parameters are also shown in the ltp_* plots for nighttime sector (1600-2400-0800 LT).

Satellite’s tracks are plotted in the geographic coordinate system at about 600 km altitude.